## Slide 1
Fitted Policy Iteration (FPI)
Fit a model that predicts the path in general (not for a specific map)
State space is continuous and high-dimensional
Value function would be extremely complicated
Instead, estimate the policy directly
Update rule
Deep Fitted Policy Iteration (DFPI)
Use a single layer feed forward neural network to improve policy approximation
References
Methods for Autonomous Path Planning
Abhi Kulgod, Anthony Degleris, Isaac Scheinfeld
Methods
Results
Motivation
Problem Setup
Randomly generated with 1-8 circular obstacles
Rejected obstacles covering endpoints.
Goal: Plan a path within the boundary and outside of the obstacles (path is a sequence of unit spaced points)
Graph Approximation and Optimization1
Approximates the best path by finding the shortest path in a space-filling graph
Uses optimization (gradient descent) to stretch and smooth, minimizing
Sigmoid represents obstacle penalty. As
gradient descent converges, we send
hardening the boundary.
[1] G. Angeris, "Some thoughts on global path optimization", 2017. [Online]. Available: https://guille.site/path-optimization-thoughts.html. [Accessed: 11- Dec- 2017].
[2] K. Gregory, V. A, V. Pong and P. Abbeel, "Uncertainty-Aware Reinforcement Learning for Collision Avoidance", 2017.
Path planning is the task of finding the optimal route between two points, avoiding any obstacles along the way
This task arises naturally in many vehicle control tasks. Our approach is modeled after drone navigation, where the goal is to find a shortest path.
Classical techniques often rely on simplifying assumptions and require a new solution each time the environment changes
A solution that makes fewer assumptions and generalizes well over different environments is preferable
Reinforcement learning techniques can implicitly learn a general solution, and have more potential for extension to dynamic environments
Algorithm | Success Rate | Average Path Length
Optimization | 1.0 | 156.4
FPI | 0.88 | 221.4
DFPI | 0.31 | 861.7
Discussion
Neural Net Architecture
Improve NN architecture to capture relevant features
Address more complex problems (moving obstacles, path smoothness constraints, etc.)
Explore fitted policy iteration further, comparing it to fitted value iteration on known problems
Future Work
Optimization
FPI
Deep FPI
Paths generated on one test map (DFPI fails)
.
We could not train any fitted value iteration model to generate a meaningful model
  WHY
The FPI model achieved surprising success
  General models for path planning are possible
  Direct policy approximation can replace value approximation in some problems
The DFPI model underperformed significantly
  Our neural network architecture failed to capture the feature complexity
Learning Curves